## Slide 1: Internet of Things

## Slide 2: Internet of Things (IoT)
Basics
  Wide variety of wireless technologies, including Bluetooth and WiFi
  Smart grids, power plants, smart homes, intelligent transportation and smart cities
  Network of physical devices for home and industrial applications
    Electronics, software, sensors, actuators and connectivity
Security
  Initially none or very weak
  Factory default usernames and passwords
  Embedded devices are sometimes hard to patch
    Can’t be updated
    Updated software not always available
    Product becomes obsolete quickly
  Devices connected to the Internet (the cloud) become vulnerable
  Website and cloud vulnerabilities become IoT vulnerabilities
Automotive is often included as a “Thing”
  Doesn’t use IoT protocols aside from Bluetooth, Cellular and WiFi
Links
  CITA: https://www.ctia.org/
  https://en.wikipedia.org/wiki/Internet_of_things

## Slide 3: IoT Protocols
Bluetooth (BT) Mesh
  https://en.wikipedia.org/wiki/Bluetooth_mesh_networking
  https://www.bluetooth.com/bluetooth-technology/topology-options/le-mesh
  Bluetooth Low Energy (BLE) available as a competitor to ZigBee
  See Bluetooth BLE section above
HaLow WiFi
  IEEE 802.11ah
  https://en.wikipedia.org/wiki/IEEE_802.11ah
  https://www.wi-fi.org/discover-wi-fi/wi-fi-halow
  Being added to new WiFi routers
  Longer range, lower power
  900Mhz
WiFi
  Wi-Fi Direct
  https://en.wikipedia.org/wiki/Wi-Fi_Direct
  https://www.howtogeek.com/180649/htg-explains-whats-the-difference-between-ad-hoc-and-infrastructure-mode/
  Like Ad-Hoc, not as secure
  Too complex for simple applications
  ESP8266, ESP32 devices provide low cost embedded WiFi

## Slide 4: IoT RFID Information
Basics
  https://en.wikipedia.org/wiki/Radio-frequency_identification
  Minimal transmission applications
  Low overhead protocols, many proprietary
  Multiple frequency bands:
    120-134Khz, 140-148Khz = LF tags, 10cm
    13.56Mhz = HF, 10-100cm
    433Mhz = UHF, good range 1-100m and low interference
    868-915Mhz = UHF, 1-2m or 300m also used for other protocols
    2.4Ghz, 5Ghz = Industrial/Scientific/Medical 1-200m – also used for Wi-Fi, BT and Zigbee
    LF has lower cost with improved range with common antennas
    HF supports more data transfer and security
  Passive Tags (Transponder)
    No power
    Power from Receiver EM field (inductive or capacitive coupling)
    Proximity Integrated Circuit Card (PICC)
  Active Tag
    Battery powered
    Can initiate exchange
    EZ-Pass, AeroScout
  Receivers
    Battery or AC powered
    Proximity Coupling Device (PCD)
  Contactless Smart Cards (RO/RW)
    Transactions (subway, parking, banking, …)

## Slide 5: IoT RFID Applications
LF Applications
  Asset tracking, antitheft, point-of-sale
  Simple identifier, but multiple standards make tag operation identification difficult
  Bike rental companies
    Customers get a RFID card at 125khz
HF Applications
  Authentication
  Point of Sale
  RFID location tracking
  Electronic toll collection (EZ-Pass, FasTrak, I-Pass, SunPass, …)
    900MHz, multiple incompatible protocols
    Attempts to standardize on IEEE 802.11p (DSRC)
    Automatic debit at tools
    Used to quietly track motorists
  Apple iBeacon
    BLE indoor positioning, up to 30m
    Apps take action based on identification of fixed location transmitters (iBeacon)
    Android supported too
    Tracking customer within retail stores
    Dynamic marketing
    Other apps can also monitor iBeacon
  UHF garment tracking
    Sewn into clothing, washer-safe
  …

## Slide 6: IoT RFID Security
Security
  Tracking/privacy attacks
  Location privacy
    Other mobile apps can use iBeacon information
    EZ-Pass gets read on highways without tollways, hidden readers (NYSDOT)
  PICC data disclosure
  Cloning cards
    Close proximity to card needed
    Many LF tags use proprietary encoding
    FCC ID lookup reveals more information
    May need to do RF analysis (SDR) and datasheets to extract tag information
  Replay attacks
  Data injection attacks
  Defeating RFID cryptography
  Optimal range is 3-5cm
  Relay attacks require 2 attacker devices over long-range wireless
    Also same kind of attack used against keyfobs

## Slide 7: IoT Near Field Communication (NFC) Basics
Basics
  https://en.wikipedia.org/wiki/Near-field_communication
  http://nearfieldcommunication.org/
  Usually 13.56Mhz
  NFC builds on HF RFID
    Use cases differ between NFC and RFID
    Unauthenticated information sharing
    Contactless payment systems
    Used in mobile phones
  Bidirectional communications
  Actively powered
  Dynamic data storage
  NFC Data Exchange Format (NDEF)
    NDEF structured data
    Type Name Format (TNF)
  Android Beam
    “Tap to Beam”
  Google Wallet
    Host Card Emulation (HEC)
    Cloud access needed
  Apple Pay
    Cloud based
    Embedded secure element, stores EMV token
    Requires pre-authorization

## Slide 8: IoT NFC Security
Security
  Same standard format across vendors
  Attacks usually associated with malformed data
  Targeted client devices
Vulnerabilities
  Android “Stagefright” malformed MP4 file
  Modifed URI data

## Slide 9: IoT RFID/NFC Hardware Tools
Tools
  ACG LAHF Reader/Writer $300
  ACS ACR122 Reader/Writer $43
    Part of SEC617 class SWAT toolkit
  HID Proxcard II
    Door access control systems
    Wiegand Protocol
  Proxmark 3 RDV2/3 $220
    Linux or Windows software
  ProxBrute
    Attempts to elevate access privileges
  Tastic RF Thief < $400
    HID MaxiProx long-range reader
    Adafruit Feather Huzzah (ESP8266 SOC)
    Saves codes to memory
    Transmit over WiFi
  Linux RFIDIOt software
    Read/write cards

## Slide 10: IoT NFC EMV
Europay, MasterCard, Visa (EMV) Cards
  ISO/IEC 14443 13.56Mhz
  Chipped credit cards
  RFID reads information similar to that of magnetic stripe
Security
  Card#, first and last name, expiration date, transaction counter
    Confidentiality exposed
  CVV2 not disclosed (Dynamic CVC)
Vulnerabilities
  Vulnerable to NFC Proxy attack
Tools
  EMV readers available
    VIVOPay
      Pwnpass application (Python script) reads out data
    Android EMV
      NFC SmartCard Info
    ACS ACR122U
      HF RFID and NFC
      Can emulate PICCs
      USB reader supported by Linux
  Linux: pwnpass, nfcproxy

## Slide 11: IoT NFC MIFARE
MIFARE
  RFID chipset built into many products
Security
  Proprietary steam cipher crypto “CRYPTO1” for authentication
  Multiple flaws
  Weak 48 bit key length
    Default key often used
  Predictable nonce values
  Recover key by eavesdropping
  Recover key from PICC, takes time under 30 minutes
  With 1 key, attacker can recover all other keys on card
  Attacker can dump card and clone
Vulnerabilities
  Mix key and UID to authenticate
  UID unique to card
  Need writable card to clone it
Tools
  Linux: mfoc, mfcuk

## Slide 12: IoT ZigBee Information
Basics
  IEEE 802.15.4
  https://standards.ieee.org/findstds/standard/802.15.4-2015.html
  https://en.wikipedia.org/wiki/Zigbee
  https://en.wikipedia.org/wiki/IEEE_802.15.4
  http://www.zigbee.org/
  Wi-Fi is too complex, Bluetooth requires excessive power and is complex
  Smart Thermostats, building controls, Keyless entry door locks, hotel management
  Radio/Protocol
    Radio Frequency For Consumer Electronics (RF4CE) up to 100m
    2.4Ghz low power, low data rate (250Kbps), long battery life, star/mesh topology
    DSSS modulation similar to 802.11b, 2.405Ghz (11ch), 2.480Ghz (26 ch), 5Mhz (16 ch)
    Small frame size of 127 bytes with max payload of 114 bytes
    Frame types: beacon, data, command, ACK
    PAN ID 16 or 64 bit (2 or 8 byte) addressing
  Devices
    Coordinator (ZC) – Authentication of nodes, hub of network (address of zero)
    Router (ZR) – Capable of forwarding frames
    Device (ZED) – Only participates
    Trust Center (TC) – Key distribution, authentication (PRO only)
    FFD vs. RFD

## Slide 13: IoT ZigBee Security
Security
  Zigbee-2006 added encryption, Message Integrity Check (MIC) support
  Zigbee-PRO adds symmetric key exchange
  Zigbee Network (NWK) layer allows encryption over entire layer
  AES-CCM of 128 bit key length with MIC
  Devices have key set at factory, no rotation or revocation, sent plaintext
  Standard security “residential” mode between Full Functional Device (FFD)
  High security “commercial” mode requires Trust Center (TC) to authenticate
  Smart Energy Profile leverages ECC for authentication and PKI for encryption
  SEC 2 in development
Vulnerabilities
  Weak replay protection
  Lack of key rotation
  Compromised device = compromised network
  Open source stack
Tools
  Killerbee tool, in Python on Linux (https://github.com/riverloopsec/killerbee)
  AVR RZ Raven USB Stick ($40), requires AVR Dragon ($60) to reflash
  GoodFET for hardware debugging, retrieving key from RAM
  Wireshark supports NWK decryption

## Slide 14: IoT Z-Wave Protocol
Basics
  https://en.wikipedia.org/wiki/Z-Wave
  https://z-wavealliance.org/
  http://www.z-wave.com/
  Not as common as ZigBee, but gaining in popularity
  900Mhz
  Mesh network
  Proprietary protocol, specification released of old version not new version
Security
  AES security options
Vulnerabilities
  Easy to reverse engineer
Tools
  RFcat firmware
  YARD Stick One
  KillerZee (similar to KillerBee)

## Slide 15: IoT Specialty Protocols
Li-Fi (Light)
  https://en.wikipedia.org/wiki/Li-Fi
  Uses light, special light bulbs
  Line of sight only
Power-line Communication
  PLC https://en.wikipedia.org/wiki/Power-line_communication
  Wired, but uses existing powerlines in a home
  Complaints are that it radiates additional RF noise into the environment
  Broadband over power grid (BPL) is uncommon and used only on low voltages (120 VAC)

## Slide 16: IoT Security
Known Exploits/Vulnerabilities
  Devil’s Ivy
    https://www.wired.com/story/devils-ivy-iot-vulnerability/
  Mirai Botnet
    Used IoT devices such as web cameras and home routers
    Used to launch some of the biggest DDoS attacks in recent history
    https://en.wikipedia.org/wiki/Mirai_(malware)
    https://www.wired.com/story/mirai-botnet-minecraft-scam-brought-down-the-internet/
    Still ongoing with new variants!
  Vulnerable devices
    Can be found on the Internet
    https://www.shodan.io/
    St. Jude Cardiac Devices
    Owlet WiFi Baby Heart Monitor
    TRENDnet Webcam
NIST Guidelines
  https://www.nist.gov/topics/internet-things-iot
  https://www.nist.gov/programs-projects/nist-cybersecurity-iot-program
  https://csrc.nist.gov/CSRC/media/Publications/nistir/8200/draft/documents/nistir8200-draft.pdf
SANS Whitepaper
  https://www.sans.org/reading-room/whitepapers/hsoffice/securing-home-iot-network-37717