## Slide 1: Keyfobs (Remote keyless system)
Basics
  Wireless keyless entry systems
  415Khz or typical RFID frequencies
Links
  https://en.wikipedia.org/wiki/Remote_keyless_system
Known Exploits/Vulnerabilities
  Samy Kamkar
  Rolljam: http://www.wired.com/2015/08/hackers-tiny-device-unlocks-cars-opens-garages/
  https://www.wired.com/2016/03/study-finds-24-car-models-open-unlocking-ignition-hack/
  https://www.wired.com/2017/04/just-pair-11-radio-gadgets-can-steal-car/
Security
  Older keyfobs are more vulnerable, susceptible to replay or relay attacks
  Should have rolling key algorithm which guards against replay attacks
    Attacker can jam vehicle and capture next message from keyfob for replay
    Mitigate with 2-way communications using challenge/response authentication
  Relay attacks are done by using a pair of devices
    One near vehicle, one near keyfob
    Communicate at long distance over wireless
    Store keyfobs in metal box (faraday cage)
  Jamming attack could be detected
  Keyfob proximity?
Future
  OEMs have used Bluetooth and some are migrating to Ultra Wide Band (UWB)

## Slide 2: Vehicle Sensors
General
  Bad weather can negatively impact and disable sensors
    https://www.accuweather.com/en/weather-news/self-driving-cars-will-they-be-safe-during-bad-weathr/60524998
    https://www.nytimes.com/interactive/2016/06/06/automobiles/autonomous-cars-problems.html
  Keeping sensors clean
    https://www.consumerreports.org/car-safety/how-to-keep-your-car-sensors-clean-in-winter/
    https://lifehacker.com/six-car-safety-sensors-you-should-always-keep-clean-dur-1756940742
  Unexpected road changes, construction
Lidar
  High detail, shorter range
  Rain or snow can confuse sensor
  Can be confused by laser pens
    https://spectrum.ieee.org/cars-that-think/transportation/self-driving/researcher-hacks-selfdriving-car-sensors
    https://www.popsci.com/g00/hackers-can-trick-lidar-used-in-autonomous-cars-with-laser-pointer?i10c.encReferrer=aHR0cHM6Ly93d3cuZ29vZ2xlLmNvbS8%3D&i10c.ua=1
Radar
  Low detail, longer range
  Can be confused by chaff and large metal obstructions
Vision (Camera)
  Varying detail and ranges, depending upon lens focus
  Image recognition is computationally intensive and not always accurate
  Can be confused by darkness or bright lighting, coloring of objects
  Road signs can be obfuscated easily
    https://arstechnica.com/cars/2017/09/hacking-street-signs-with-stickers-could-confuse-self-driving-cars/